## Slide 1: CSC3050 –Computer Architecture
Code (Instruction) Scheduling

## Slide 2: Why Rearrange Code Sequence?
IF
ID
EX
Mem
WB
lw X8, a
lw X9, b
mul X10,X8,X8
add X11,X9,X10
Clock 0
Clock 1
Clock 2
Clock 3
Clock 4
Clock 5
Clock 6
Clock 7
Clock 8
lw X12,c
add X13,X9,X0
beq X11,X0,L1

## Slide 3: Bubbles in Pipeline
IF
ID
EX
Mem
WB
Clock 0
Clock 1
Clock 2
Clock 3
Clock 4
Clock 5
Clock 6
Clock 7
Clock 8
Data and Control
hazards generate bubbles in the pipeline, reducing execution efficiency

## Slide 4: Rescheduling Reduces Bubbles
More efficient execution after rescheduling
IF
ID
EX
Mem
WB
Clock 0
Clock 1
Clock 2
Clock 3
Clock 4
Clock 5
Clock 6
Clock 7
Clock 8
lw X8, a
lw X9, b
mul X10,X8,X8
add X11,X9,X10
lw X12,c
add X13,X9,X0
beq X11,X0,L1

## Slide 5: Dependence DAG: Scheduling Constraints
1 lw $pr1, a
2 lw $pr2, b
3 add $pr3, $pr1,$pr2
4 mul $pr4, $pr3, 3
5 mul $pr5, $pr1, $pr2
add $pr6, $pr4, 2
sw $pr6, 0($pr5)
lw $pr1, c
lw $pr7, d
sw $pr7, 0($pr4)
add $pr8,$pr7,$pr1
1
2
3
4
5
6
7
8
10
9
11
Each node represents an instruction Each arc represents a dependence
DAG:
Directed
Acyclic
Graph

## Slide 6: Three Types of Register Data Dependence
1
2
3
4
5
6
7
8
10
9
11
Flow dependence (RAW)
Anti-dependence
(WAR)
Output-dependence
(WAW)

## Slide 7: Memory Dependency (due to potential aliasing)
1 lw $pr1, a
2 lw $pr2, b
3 add $pr3, $pr1,$pr2
4 mul $pr4, $pr3, 3
5 mul $pr5, $pr1, $pr2
add $pr6, $pr4, 2
sw $pr6, 0($pr5)
lw $pr1, c
lw $pr7, d
sw $pr7, 0($pr4)
add $pr8,$pr7,$pr1
1
2
3
4
5
6
7
8
10
9
11

## Slide 8: Memory Dependency (due to potential aliasing)
1 lw $pr1, a
2 lw $pr2, b
3 add $pr3, $pr1,$pr2
4 mul $pr4, $pr3, 3
5 mul $pr5, $pr1, $pr2
add $pr6, $pr4, 2
sw $pr6, 0($pr5)
lw $pr1, c
lw $pr7, d
sw $pr7, 0($pr4)
add $pr8,$pr7,$pr1
1
2
3
4
5
6
7
8
10
9
11
Scheduling memory instructions can be quite challenging:
Memory dependencies may be unknown
Memory latencies are often unknown
Speculative load/store may trap
Memory resources are often shared:
DRAM
Bus
Interconnection network
Volatile variables (in OS kernels)
and more ….

## Slide 9: A Legal Schedule
1
2
3
4
5
6
7
8
10
9
11
Any topological sort of the DAG will represent a correct schedule.
Topological sort is the enumeration of the nodes in which each node appears before its children.
Some legal schedules:
1,2,3,5,9,4,8,6,10,11,7
9,1,2,3,4,10,6,5,8,7,11

## Slide 10: A Legal Schedule
1
2
3
4
5
6
7
8
10
9
11
Any topological sort of the DAG will represent a correct schedule.
Topological sort is the enumeration of the nodes in which each node appears before its children.
Some legal schedules:
1,2,3,5,9,4,8,6,10,11,7
9,1,2,3,4,10,6,5,8,7,11
Code scheduling involves listing all legal schedules and choosing
the best one.
This seems easy! However, the number of permutations could grow exponentially!
If there are N instructions, possible schedules could be N!
For example, if N is 50, N! = 3 x 10^64
if N is 100, N! = 9 x 10^158

## Slide 11: Operation Latency: Weight of Arcs
1
2
3
4
5
6
7
8
10
9
11
2
2
2
2
1
3
1
3
2
2
2
3
Weight indicates the
operation latency
Here we assume a
Load takes 2 cycles
Multiply takes 3 cycles
Add takes 1 cycle

## Slide 12: Critical Paths
1
2
3
4
5
6
7
8
10
9
11
2
2
2
2
1
3
1
3
2
2
2
3
General guideline:
Nodes on the critical paths
should be scheduled
as early as possible

## Slide 13: Identify Critical Paths
1 (7)
2 (7)
3(5)
4(4)
5 (3)
6 (1)
7 (0)
8 (2)
10 (0)
9 (2)
11 (0)
2
2
2
2
1
3
1
3
2
2
2
3
Traversing the DAG from the leaves towards the roots labeling each node with the maximum possible delay from that node to the end of the block. (Reverse Topological Sort)
Maximum delay of each node is computed as:
MD = max ( each child’s MD + arc_weight )

## Slide 14: Mark each node with Maximum Delay (yellow number)
1 (7)
2 (7)
3(5)
4(4)
5 (3)
6 (1)
7 (0)
8 (2)
10 (0)
9 (2)
11 (0)
2
2
2
2
1
3
1
3
2
2
2
3
0
0
1
1
3
3
4
3
5
7
7

## Slide 15: List Scheduling
Basic Block scheduling
Build Dependence DAG
Mark each node with maximum delay to the end of block
Traverse the DAG from the root toward the leaves, selecting nodes from a candidate list to schedule. Keep tracking of the current cycle to minimize possible stalls.

## Slide 16: Commonly Used Heuristics
The following heuristics are often used
  Favor nodes that can start without stalling
  If there is a tie, favor nodes with the maximum delay to the end of the block
  If there is a tie,
    Favor the original order
    Favor nodes that have a large number of children
    Favor nodes that are the final use of a reg

## Slide 17: Example
1 (7)
2 (7)
3(5)
4(4)
5 (3)
6 (1)
7 (0)
8 (2)
10 (0)
9 (2)
11 (0)
2
2
2
2
1
3
1
3
2
2
2
3
Candidate list ={1, 2, 9}
Select 1,
Select 2,
Clist = {3,5,9}
Select 9 – why?
Clist = {3,5}
Select 3 – why?
Clist = {4,5}
Select 4
Clist = {6,10,5}
Select 5
Clist = {6,10,8}
Select 8
Clist = {6,10,11}
Select 6

## Slide 18: Execution Cycle Comparison
1 lw $pr1, a
2 lw $pr2, b
3 add $pr3, $pr1,$pr2
4 mul $pr4, $pr3, 3
5 mul $pr5, $pr1, $pr2
add $pr6, $pr4, 2
sw $pr6, 0($pr5)
lw $pr1, c
lw $pr7, d
sw $pr7, 0($pr4)
add $pr8,$pr7,$pr1
1 lw $pr1, a
lw $pr2, b
9 lw $pr7, d
3 add $pr3, $pr1,$pr2
4 mul $pr4, $pr3, 3
mul $pr5, $pr1, $pr2
8 lw $pr1, c
add $pr6, $pr4, 2
10 sw $pr7, 0($pr4)
7 sw $pr6, 0($pr5)
11 add $pr8,$pr7,$pr1
0 1 3 4 5 7 8 9 10 12 13
0 1 2 3 4 5 6 7 8 9 10
Original code
Scheduled code
Issue cycle
Issue cycle