## Slide 1: CSC3050 – Computer Architecture RISC-V Instruction Set Architecture
Prof. Wei Chung Hsu
School of Data Science
Chinese University of Hong Kong, Shenzhen

## Slide 2: Assembly Language Instructions
The language of the machine
  Want an ISA that makes it easy to build the hardware and the compiler
Our focus: the RISC-V ISA (or RV in short)
Design Goals:
  Maximize performance, minimize cost, reduce design time (time-to-market), minimize memory space (embedded systems), and minimize power consumption (mobile systems).
  ISA should be scalable, flexible, and extensible
Notes: Scalable: micro-controller, embedded systems, mobile computers, desktops, servers, main frame, warehouse scale, supercomputers.
Flexible: Used for various applications. Not just for scientific computation. GPU cannot work well for general applications, does not support Pcalls, branches.
Extensible: extensions

## Slide 3: CISC vs. RISC
Complex Instruction Set Computer (CISC)
  Implement complex instruction directly by hardware (horizontal micro-code vs vertical micro-code)
  Lots of instructions of variable size, optimized for memory size, typically fewer registers. (require large micro-store size)
  E.g. IBM 360, Intel x86, DEC VAX. Dominant before 80’s
Reduced Instruction Set Computer (RISC)
  Fixed size instructions, more registers, optimized for pipelined implementation.
  Usually called a “Load/store” architecture, only load/store instructions access memory.
  RISC-V, MIPS, Sun SPARC, HP PA-RISC, IBM PowerPC, ARM
Notes: According to the design principle of the instruction set architecture, x86 has 15 addressing mode. X86 has variable length instructions, from 1 byte to 15 bytes.
Calls is a representative CISC instruction. Calls is a subroutine call, it also handle argument count, passing argument, set up stack frame, store return address and save all used registers.
Why was the debate interesting? If you follow the argument/counter arguments, you have learned a lot about computer technology.
One scientist predicted “All future binaries will be in x86, but all processors will be implemented in RISC.”
RISC-V has only four: base+offset, reg-reg, PC-relative, Register indirect.
X86 has 8 registers, DEC VAX has 16

## Slide 4: RISC – Reduced Instruction Set Computer
RISC Philosophy
  fixed instruction lengths
  load-store instruction sets
  limited number of addressing modes
  small number of simple operations
  easier for pipelined implementation
Instruction sets are measured by how well compilers use them as opposed to how well assembly language programmers use them.
Notes: If CS students do not speak assembly language, who will translate HLL? Who will debug?

## Slide 5: RISC – Reduced Instruction Set Computer
RISC Philosophy
  fixed instruction lengths
  load-store instruction sets
  limited number of addressing modes
  small number of simple operations
  easier for pipelined implementation
Instruction sets are measured by how well compilers use them as opposed to how well assembly language programmers use them.
Most machines, including RISCs, have more
than one size instructions
To support AI/ML/DL/LLM, fast matrix multiplications
are important, such new instructions are not simple.
Notes: If CS students do not speak assembly language, who will translate HLL? Who will debug?

## Slide 6: CISC vs. RISC
Complex Instruction Set Computer (CISC)
  Implement complex instruction directly by hardware (horizontal micro-code vs vertical micro-code)
  Lots of instructions of variable size, optimized for memory size, typically fewer registers. (require large micro-store size)
  E.g. IBM 360, Intel x86, DEC VAX. Dominant before 80’s
Reduced Instruction Set Computer (RISC)
  Fixed size instructions, more registers, optimized for pipelined implementation.
  Usually called a “Load/store” architecture, only load/store instructions access memory.
  RISC, MIPS, Sun SPARC, HP PA-RISC, IBM PowerPC
Key trade-off
CISC: More complex Hardware, simpler Software
RISC: Simpler Hardware, more complex Software
Notes: According to the design principle of the instruction set architecture, x86 has 15 addressing mode. X86 has variable length instructions, from 1 byte to 15 bytes.
Calls is a representative CISC instruction. Calls is a subroutine call, it also handle argument count, passing argument, set up stack frame, store return address and save all used registers.
Why was the debate interesting? If you follow the argument/counter arguments, you have learned a lot about computer technology.
One scientist predicted “All future binaries will be in x86, but all processors will be implemented in RISC.”
RISC-V has only four: base+offset, reg-reg, PC-relative, Register indirect.
X86 has 8 registers, DEC VAX has 16

## Slide 7: Some RISC Design Principles
Simplicity favors regularity
  Fixed size instructions
  Small number of instruction formats
  Opcode always the first several bits
Smaller is faster
  Limited instruction set
  Limited number of registers
  Limited number of addressing modes
Make the common case fast
  Arithmetic operands from the registers (load-store machine)
  Allow instructions to contain immediate operands
Good design demands good compromises
  Instruction format and number of operands supported.
KISS Principle:
Keep It Simple! Stupid!
“You can please some of the people all of the time, you can please all of the people some of the time, but you can’t please all of the people all of the time.”
Tradeoff unavoidable!!
Quote from Lincoln
Notes: Design for pipelined implementations
Stupid not an insult, but as a reminder to avoid overcomplicate things
Compromise:
Large register – reduces memory accesses, but increases instruction size
Instructions allow memory operands: some advantages, but may get to very nasty simulations

## Slide 8: RISC-V
The new, open standard, license/royalty-free ISA
Several variants of RV
  RV32, RV64, RV128 – Different data widths (addressing capability)
  ‘I’ – Base Integer instructions, ‘E’ – Base for embedded systems (e.g. only 16 regs)
  ‘M’ – Multiply and Divide, ‘A’ – Atomic memory instructions
  ‘C’ – Compressed extension, with 16b instructions
  ‘F’ and ‘D’ – Single and Double precision floating point
  ‘V’ – Vector extension
  And many other modular extensions
We will design a pipelined RV32I processor simulator (Project#3) with a cache simulator (project #4).
The abbreviation letters following RV must follow the defined order
  Base Implementation (I or E), Standard extensions, more Standard ext., Non-standard ext.
Notes: Apple. Samsung, Qualcomm pay license upfront. E base implementation has 16 reg, 40 instructions, fewer shift instructions, does support for 16b instructions.
MTK pay royalty
We do not study VE in this course, if you are interested, 6031 will do that

## Slide 9: RV32I Register State (Architecture State)
32 general purpose registers (GPR)
  x0, x1, …, x31
  32-bit wide integer registers
  x0 is hard-wired to zero
Program counter (PC)
  32-bit wide
CSR (Control and Status Registers)
  User-mode
    cycle (clock cycles) // read only
    instret (instruction counts) // read only
  Machine-mode
    hartid (hardware thread ID) // read only
    mepc, mcause etc. used for exception handling
  Custom
    mtohost (output to host) // write only – custom extension
In RISC-V, Hart refers to
a hardware thread, which
is often a “core” in a multicore
chip.
Architecture states must be saved,
at context switches (e.g. a
process switch, an interrupt, …).
So that the program may resume!
Notes: X register , X means flexibility, extensibility, no implication like A,S,B,T,F, R, V

## Slide 10: X0 is always zero
Why?
  Constant zero is often used in instructions. Having X0 as zero can save one instruction to clear a register.
    e.g. A = - B // suppose B is in X8
    Without X0 as 0 With X0 as 0
    XOR X10, X10, X10 SUB X9, X0, X8
    SUB X9, X10, X8
  Copy X2 to X1 is simply
    ADD X1, X0, X2
  Compare and branch instructions often need one operand to be 0.
    There are no immediate forms in branch instructions
  Some RISC architectures even use load to x0 as memory hints
    e.g.
  cache prefetching
Can I use ADDi X1, X2,0 ?

## Slide 11: Instruction Types (based on functionality)
Register-to-Register Arithmetic and Logical operations (ALU)
Control Instructions alter the sequential control flow (B and J)
Memory Instructions move data to and from memory (Memory)
CSR Instructions move data between CSRs and GPRs; the instructions often perform read-modify-write operations on CSRs (Privileged)
Privileged Instructions are needed by the operating systems and can only be executed under kernel (or system) mode. User programs in user mode cannot execute them.
Notes: Privileged instructions: interrupt, memory management, system calls, CSR, mode change

## Slide 12: Instruction Types (based on format)
R, I, B, J
12b immed: I and B
B has no “rd” field
No immediate: R
20b immed: J

## Slide 13: Instruction Formats (R-type)
funct7
rs2
funct3
rs1
rd
opcode
7
5
5
3
5
7
R-type instruction
source
register
destination
register
R-type | funct7 | RS2 | RS1 | funct3 | RD | Opcode | Example
ADD | 0000000 | 00011 | 00010 | 000 | 00001 | 0110011 | Add x1,x2,x3
SUB | 0100000 | 00011 | 00010 | 000 | 00001 | 0110011 | Sub x1,x2,x3

## Slide 14: ALU Instructions (R)
Register-Register instructions (R-type) (opcode=0110011)
  opcode=OP: rd  rs1 (funct3, funct7) rs2
  funct3 = ADD/SLT/SLTU/AND/OR/XOR/SLL
  funct3= ADD (000)
    funct7 = 0000000: rs1 + rs2
    funct7 = 0100000: rs1 – rs2
  funct3 = SRL (101)
    funct7 = 0000000: logical shift right
    funct7 = 0100000: arithmetic shift right
funct7
rs2
funct3
rs1
rd
opcode
7
5
5
3
5
7

## Slide 15: Instruction Formats (I-type)
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
I-type instruction & I-immediate (32 bits)
I-imm = signExtend(inst[31:20])
I-type | immediate | RS1 | funct3 | RD | Opcode | Example
addi | 010000000000 | 00010 | 000 | 00001 | 0010011 | Addi x1,x2,1024
ld | 001111101000 | 00010 | 000 | 00001 | 0110011 | Ld x1, 1000(x2)
Notes: How to know 001111101000 is 1000? 1024 is 010000000000, get the inverse of 1111101000  0000010111+1 = 24, so 1024 -24 is 1000

## Slide 16: ALU Instructions (I)
Register-immediate instructions (I-type) (0010011 for alu, 0000011 for load)
  opcode = OP-IMM: rd  rs1 (funct3) I-imm
  I-imm = signExtend (inst[31:20])
  funct3 = ADDI/SLTI/SLTIU/ANDI/ORI/XORI
A slight variant in coding for shift instructions - SLLI / SRLI / SRAI
  rd  rs1 (funct3, inst[30]) I-imm[4:0]
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
To distinguish logical shift and arithmetic shift
shamt (shift amount)
5bit for RV32
6bit for RV64
Notes: What is the role of inst[30]?

## Slide 17: Load Instructions (I)
Load (I-type)
  opcode = LOAD: rd  mem[rs1 + I-imm]
  I-imm = signExtend(inst[31:20])
  funct3 = LW/LB/LBU/LH/LHU
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
Base + Offset
Array
Struct
Linked list
Notes: Ignore byte and half word instructions: LB, LBU, LH, LHU, SB, SH

## Slide 18: Load Instructions (I)
Load (I-type)
  opcode = LOAD: rd  mem[rs1 + I-imm]
  I-imm = signExtend(inst[31:20])
  funct3 = LW/LB/LBU/LH/LHU
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
Be aware! There is no lwu in RVI32
Examples:
LW x31, -4(fp) // local variable
LW x1, 4(x2) // struct element
LW x0, 4(x2) // hint
LW x5, 0(x2) // array A[i]; x2=base+index
Load from a local variable c
LW X1, -4(fp)
Load from an array d[0]
LW X1, -20(fp)
Load from d[1]
LW X1, -16(fp)
Int x(int a,b) {
Int c;d[4];
a=c+d[0]…;}
c
fp
d[3]
d[2]
d[1]
d[0]
Notes: Ignore byte and half word instructions: LB, LBU, LH, LHU, SB, SH

## Slide 19: Instruction Formats (S-type)
S-type instruction & S-immediate (32 bits)
imm[11:5]
rs2
funct3
rs1
imm[4:0]
opcode
7
5
5
3
5
7
S-imm = signExtend({inst[31:25], inst[11:7]})
S-type | immediate | RS2 | RS1 | funct3 | immed | Opcode | Example
sw | 0011111 | 00001 | 00010 | 010 | 01000 | 0100011 | sw x1, 1000(x2)
SW needs two operands, rs1 and rs2. In I-type instructions, rs2 is not used. So rs2 is part of the 12b immediate field. Here, rs2 is used, so the 12b immediate is split into two parts; one part (5b) goes to rd, and 7b remains in the original immediate field.

## Slide 20: Store Instructions (S)
Store (S-type)
  opcode = STORE: mem[rs1 + S-imm]  rs2
  S-imm = signExtend({inst[31:25], inst[11:7]})
  funct3 = SW/SB/SH
imm[11:5]
rs2
funct3
rs1
imm[4:0]
opcode
7
5
5
3
5
7
Examples:
SD x31, 1000(x2)
SW x1, 0(x2)
SW x0, 4(x2)
SB x1, 1(x2)

## Slide 21: Store Instructions (S)
Store (S-type)
  opcode = STORE: mem[rs1 + S-imm]  rs2
  S-imm = signExtend({inst[31:25], inst[11:7]})
  funct3 = SW/SB/SH
imm[11:5]
rs2
funct3
rs1
imm[4:0]
opcode
7
5
5
3
5
7
Examples:
SD x31, 1000(x2)
SW x1, 0(x2)
SW x0, 4(x2)
SB x1, 1(x2)
Store to a local variable c
Sw X1, -4(fp)
Store to array d[0]
Sw X1, -20(fp)
Store to d[1]
Sw X1, -16(fp)
Int x(int a,b) {
Int c;d[4];
c=d[0]=…;}
c
fp
d[3]
d[2]
d[1]
d[0]

## Slide 22: Pop Quiz
The target architecture of this course is
  RVI64
  RVI32
  RV32E
  RV32I
  Answer : C) RV32I

## Slide 23: Pop Quiz
When we say RV32I, what does it mean by 32?
  The general register width is 32 bit
  The number of register is 32
  The addressability is 32 bit
  The instruction length is 32 bit
  Answer : (A) and (C)

## Slide 24: Data Alignment
Natural alignments: Data elements of a specific size should be stored at memory addresses that are multiples of that size. For example, SW/LW reference addresses are multiple of 4. SD/LD reference addresses are multiple of 8. SB/LB will always be aligned.
Aligned data references simplify the hardware
  No cache line crossing (may need multiple accesses to get the data); no double TLB misses; no double page faults come from a single memory instruction execution.
  Better cache line utilization
Most RISC machines (MIPS, ARM, PowerPC, HP-PA, …) enforce data alignments.
RISC-I to RISC-V do not explicitly enforce data alignments. But their compilers often enforce data alignments. For example, for the following data structure,
struct { int a; long long b; char c; double d);
the compiler will lay each field as a: 0 b: 8
(numbers are offsets to the struct) c: 16 d: 24

## Slide 25: Data Alignment Avoids Boundary Crossing
In computer architectures, memory is often managed as a unit of cache lines and memory pages.
Cache lines are typically 64 bytes. Other sizes are also frequently used, such as 32 bytes and 128 bytes.
Memory is managed as a unit of pages; common page sizes are 4KB, 16KB, and larger.
If data are always naturally aligned, a memory reference will not cross a line or page boundary.
Crossing a boundary makes the memory reference difficult to handle. The hardware needs to go through two exceptions instead of one.

## Slide 26: Three Operand Instruction Format
Zero and One operand instruction format
  Stack architecture. All operations (add/sub…) are taking operands from the top of the stack. Those are 0-operand instructions.
  Push and Pop are 1-operand instructions. They move data between the memory and the stack.
Two operand instruction format
  A = A op B, one of the source operands must be identical to the destination.
Three operand instruction format
  A = B op C
Four operand instruction format
  A = B op C op D, for example, A = B*C + D. This is the most frequently used instruction in matrix multiplication. RISC-V F/D extension has added this fused-mul-add instruction with a new R4 (4 registers) instruction type.
funct7
rs2
funct3
rs1
rd
opcode
2
5
5
3
5
7
rs3
5
Notes: Introduced inn 2019/12.

## Slide 27: Fused-Multiply-Add (FMA) instruction
RISC-V favors “simplicity” and “regularity”, so why does it include the four-operand instructions? Is breaking the RISCy philosophy worthwhile?
This instruction (FMA) is extremely important for the F/D (Floating Point) extension.
  It is applicable to the most commonly used linear algebra operation: matrix multiply
    In the inner loop: C[i][j] = C[i][j] + A[i][k] * B[k][j]
  It can substitute two instructions: reduce half of the instructions
  It computes faster: two FP roundings can be saved.
  Its result is more precise: two FP roundings can be skipped
  Most newer machines include this instruction.

## Slide 28: Logical/Shift Operations in RISC-V
Logical operations | C operators | Java operators | RISC-V instructions
Shift Left | << | << | SLL, SLLi
Shift Right | >> | >>> | SRL, SRLi
Shift right arithmetic | >> | >> | SRA, SRAi
Bitwise AND | & | & | AND, ANDi
Bitwise OR | I | I | OR, ORi
Bitwise XOR | ^ | ^ | XOR, XORi
Bitwise NOT | ~ | ~ | XORi with -1

## Slide 29: SRL (logic) or SRA (arithmetic) ?
SRA will fill with the sign bit to preserve the negative values of 2’s complement. SRL will fill with zeros.
In Java, >>> means SRL, and >> means SRA
In C, both shifts use the same operator: >>. The compiler chooses SRA for signed data types and SRL for unsigned ones.
e.g.
-4 >> 2
1111….100 Shift right by 2: SRL (Logical shift)  00111…111
SRA (Arithmetic shift)  1111….111

## Slide 30: Masked Operations
If you only want the lower 10 bits of a variable A, or
If you want to get the remainder of A div by 1024
  A and 1023 (i.e. 0000….1111111111)
If you want to get rid of the lower 10 bits of A
  A and (1111…..1110000000000)
Setting specific bits in a word (e.g., the 3rd and 4th bits)
  OR ….0001100

## Slide 31: Instruction Formats SB, U, J
SB-type instruction & B-immediate (32 bits)
imm[12]
imm[10:5]
rs2
rs1
funct3
imm[4:1]
imm[11]
opcode
1
6
5
5
3
4
1
7
B-imm = signExtend({inst[31], inst[7], inst[30:25], inst[11:8], 1’b0})
U-type instruction & U-immediate (32 bits)
rd
opcode
5
7
imm[31:12]
20
U-imm = signExtend({inst[31:12], 12’b0})
UJ-type instruction & J-immediate (32 bits)
imm[20]
imm[10:1]
rd
imm[19:12]
imm[11]
opcode
1
10
1
8
5
7
J-imm = signExtend({inst[31], inst[19:12], inst[20], inst[30:21], 1’b0})

## Slide 32: Branch Instructions (SB)
e.g. beq x1,x2, Label
Branches read two registers, compare them, and determine whether the branch should be taken or fall through.
The instruction type is SB, which is similar to S type. There is no destination register operand, rd. However, immediate is composed in different ways.
Branches are used for loops and if-then-else control statements.
Function calls and jumps are handled with JAL (J-format)
Branch targets are encoded as offset to the current PC (Program Counter), called PC-relative addressing.
Notes: Branch is called conditional jump

## Slide 33: PC-relative Addressing
Use the immediate field as a 2’s complement offset to PC.
  Branch instructions change the PC by a small amount.
    either PC+4 or PC+offset
  Can specify ± different addresses from the PC
  In the S-type (store instruction), the offset is relative to the base address, in SB-type (branch), the offset is relative to PC.
  For store instructions, the offset is in bytes, for branch instructions, the offset is in two bytes (half word). Why? Because RV instructions are either 32b (regular) or 16b (compressed, as in the C extension) , the branch range can be doubled using two bytes as a unit. (unfortunately, not quadrupled)

## Slide 34: Scaling Branch Offsets
If all instructions are words (32b), we could scale the immediate value by 4x, before adding to the PC. This would allow one branch instruction to reach ± X 32b instructions either side of PC.
If branch taken: PC = PC + immediate * 4
If branch fall through: PC = PC + 4
Due to the support for 16b instructions (required by C extension), the ISA decides to only scale the immediate by 2 (2 bytes).
In summary, RV branch instructions can only reach ± X 32b instructions.
Q: How to reduce the instruction from 32b to 16b?
± 4KB
Notes: (In Compressed format, Opcode reduced to 2b, immediate reduced to 8b, must use implicit or implied registers

## Slide 35: Branch Instruction
imm[12]
imm[10:5]
rs2
rs1
funct3
imm[4:1]
imm[11]
opcode
1
6
5
5
3
4
1
7
B-imm = signExtend({inst[31], inst[7], inst[30:25], inst[11:8], 1’b0})
Loop: beq x19,x10,end
add x19,x18,x10
addi x19,x19,-1
j loop
end: //branch target
What is the branch offset?
16
How to encode it ?
Intuitively: 000000001000 0
0
000000
rs2
rs1
funct3
1000
0
opcode
1
6
5
5
3
4
1
7
Notes: You do not need to know the details of such encoding.

## Slide 36: Why Different Immediate Encoding in S and B
imm[12]
imm[10:5]
rs2
rs1
funct3
imm[4:1]
imm[11]
opcode
1
6
5
5
3
4
1
7
B
S
imm[12:6]
rs2
funct3
rs1
imm[5:1]
opcode
7
5
5
3
5
7
imm[12]
imm[11]
imm[10:5]
imm[4:1]
0
imm[12]
imm[11:6]
imm[5:1]
Address to instruction
(in 16 bits)
Address to data
(in 8 bits)
Sign bit: same
Imm[10:1] same
Imm[11] for B comes from inst[7], for S comes from inst[30]
Imm[0] for B is always 0, for S comes from inst[7]
Notes: You do not need to know the details of such encoding.

## Slide 37: What if the branch target is >
RV branch instructions can only reach ± X 32b instructions.
If the target is more than instructions away, we must resort to the JUMP instruction, which can reach instructions, or ytes
Example:
beq X10, X0, far_away bne x10, x0, NEXT_LABEL
next-inst j far_away
NEXT_LABEL: next-inst
Notes: What if jump is not far enough? Use JALR indirect jump, the register can contain all 32b address, what if that is not enough? Goto 64b

## Slide 38: LUI and AUIPC Instructions
Register-immediate instructions (U-type)
  opcode = LUI : rd  U-imm
  opcode = AUIPC: rd  pc + U-imm
  U-imm = {inst[31:12], 12’b0}
  AUIPC can be used in conjunction with the JALR instruction to jump to a faraway place (greater than ±1MB). However, this is not ideal for binary patching (modern software like patching to modify executables on the fly)
rd
opcode
5
7
imm[31:12]
20

## Slide 39: How to load a 32b const into a register?
Assuming the constant is 0x12345678 (Hexadecimal number)
Option 1: store the constant in memory, then use a LW (load word) instruction. (load instruction is usually expensive)
Option 2: use the LUI and ADDI instruction pair.
  lui X1, 0x12345 (move the 20b value to the upper 20b in X1)
  addi x1, 0x678 (add the lower 12 bits to X1)
0x12345
20
X1
12
0x678
0x12345
20
X1
12

## Slide 40: Corner case (when the 12b is > 0x800)
What if the constant is 0x12345800 (Hexadecimal number)
  lui X1, 0x12345 (move the 20b value to the upper 20b in X1)
  addi x1, 0x800 (add the lower 12 bits to X1)
0x12345
20
X1
12
0x800
0x12345
20
X1
12
addi x1,100000000000
The sign bit is on, and the immediate is sign extended
So the value becomes FFFFF8000 in the 32b temporary register !! Bad news!!
Some adjustments are needed. (perhaps add 1 to 0x1235, make it to 0x12346).
Don’t worry about this, just use the
Li X1, 0x12345800 pseudo instructions, the assembler will handle the needed adjustments.

## Slide 41
Compiling two C statements into RV
Example:
1) a = b + c; d = a – e; 2) f = (g+h) – (i+j)
add a, b, c add t0, g, h
sub d, a, e add t1, i, j
sub f, t0, t1
add x1, x2, x3 add x5, x20, x21
sub x4, x1, x5 add x6, x22, x23
sub x19, x5, x6
f  x19
g  x20
h  x21
i  x22
J  x23
Note that registers
can be allocated to
scalar variables or
temporaries.

## Slide 42
Memory Operands
Simple variables may be allocated in registers. How about complex data structures such as arrays, strings, and structures?
Arrays, structures, and strings will be stored in the memory.
We specify the address of the data we need and use load instructions to move it to registers.
For example, to reference A[8], suppose A is a 32b integer array, with the starting address stored in register X1. Then, the following load-word instruction will be used:
lw X2, 32(X1); 32 is the offset to the base address.
The offset is calculated as 4 x 8 (4 is the word size, and 8 is the index of array A). RV does not use 8(X1), because most machines use byte addresses rather than word or double word addresses.

## Slide 43
Exercises
Suppose A is a 64b long long int array, with the starting address stored in register X1. what instruction should be used to access A[100]?
1) LW X2, 100(X1)
2) LB X2, 800(x1)
3) LD X2, 800(X1)
Struct S1 { int green; int red; int blue} A[];
Suppose A is an array of structure S1, and the starting address of A is stored in register X1. what instruction should be used to access A[100].red?
1) LW X2, 100(X1)
2) LW X2, 1204(x1)
3) LW X2, 1200(X1)
4) LW X2, 104(X1)
3
2

## Slide 44
A More Challenging Exercises
Struct S1 { int white; long long count; char c; int red; int blue } A[];
Suppose A is an array of structure S1, and the starting address of A is stored in register X1. what instruction should be used to access A[100].red?
1) LW X2, 2817(X1)
2) LW X2, 3220(x1)
3) LW X2, 2820(X1)
4) LW X2, 3617(X1)
5) LW X2, 2020(X1)
2
4, pad 4, 8, 1, pad 3, 4, 4 Total 28,
Struct size must be multiple of the largest field, so Total size is 32

## Slide 45: Jump Instructions
  Unconditional jump and link (UJ-type)
  opcode = JAL: rd  pc + 4; pc  pc + J-imm
  J-imm = signExtend({inst[31], inst[19:12], inst[20], inst[30:21], 1’b0})
  Jump ±1MB range
  To reach a range greater than 1MB, AUIPC+JALR is needed.
Unconditional jump via register and link (I-type)
  opcode = JALR: rd  pc + 4; pc  (rs1 + I-imm) & ~0x01
  I-imm = signExtend(inst[31:20])
imm[20]
imm[10:1]
rd
imm[19:12]
imm[11]
opcode
1
10
1
8
5
7
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
Indirect-Jump
A location in a jump table
Jump table stores multiple
jump instructions or addresses
Notes:   Effect of ~0x01

## Slide 46: Why Different Immediate Encoding in U and J
U
J
imm[31:12]
rd
opcode
5
7
imm[31:20] imm[19:12]
20
imm[11:1]
imm[20]
imm[10:1]
rd
imm[19:12]
imm[11]
opcode
1
10
1
8
5
7
imm[11:1]
U
J
Notes: You do not need to know the details of such encoding.

## Slide 47
Why Jump and Link? Why no Normal Jumps?
RISC-V has only Jump and Link instruction:
  Two variations: JAL (direct) and JALR (indirect)
What happens to a normal jump? Is the link register wasted?
  There is a pseudo instruction “J”, which the assembler will set the “rd” as 0
  If not using the pseudo instruction “J,” the compiler can still discover the link register is unused and reuse it for another purpose.
This helps to avoid using additional jump instructions, such as one for call and one for jump. This is related to simplicity and regularity.
But normal jumps do not need “rd”, so “rd” field could be used for immediate, and this could increase the jump range (32x greater)
  This calls for another instruction format (25 bits of immediate) is it worthwhile?

## Slide 48
JALR Instruction
JALR is an indirect branch. This instruction is in I-type. It is usually used for addresses computed at runtime (such as return addresses, functional pointers, etc.).
JALR: rd  pc + 4; // set up link
    pc  (rs1 + I-imm) & ~0x01 // branch to target
For return branch:
pc  (rs1) & ~0x01 // byte address in rs1
For branch table:
pc  (rs1 + I-imm) & ~0x01 // jump to one entry in the branch table, which is another jump instruction.
The hardware does not distinguish a return branch from a branch to the first entry of the branch table. In both cases, the offset is 0, i.e. 0(rs1).
Notes: JALR on Register is usually implemented as return jump or jump to functions (Function pointer passed in as a parameter)

## Slide 49
How to infer a return branch?
Why does the hardware want to know whether the indirect jump-and-link (JALR) is a return branch?
  This is related to how to predict the return target address.
  Many machines implement the return address stack: a call pushes the return address on the stack, and a return pops the top entry of the return address stack and uses the popped address as the predicted return address.
So, how does the hardware identify a return instruction?
  One possibility is to use the calling convention that the link register is usually X1. So, a JALR 0(X1) instruction can be assumed to be a return instruction.
  This prediction could be wrong if the compiler sets a starting address of a jump table in X1, and the indirect jump is going to the first entry of the jump table.
Notes: JALR on Register is usually implemented as return jump or jump to functions (Function pointer passed in as a parameter)

## Slide 50: More About Branches
Conditional branches (SB-type)
  opcode = BRANCH: pc  compare(funct3, rs1, rs2) ? pc + B-imm : pc + 4
  B-imm = signExtend({inst[31], inst[7], inst[30:25], inst[11:8], 1’b0})
  Jump 4KB range
  funct3 = BEQ/BNE/BLT/BLTU/BGE/BGEU
imm[12]
imm[10:5]
rs2
rs1
funct3
imm[4:1]
imm[11]
opcode
1
6
5
5
3
4
1
7
We have BLT, BGE, but
Why there are no
BLE
BGT instructions?
Does this break the regularity?
To implement BG, you may simply swap the operands of the BLT instruction:
BLE X1,X2, label  BG X2,X1, label
Checking 0 <= x < y (is x in bound) usually
takes two instructions:
If (x <= 0) || (x > y)
However, if you treat x and y as unsigned
one check would be sufficient
BGEU X, Y

## Slide 51: Instructions to Read and Write CSR
  opcode = SYSTEM
  CSRW rs1, csr (funct3 = CSRRW, rd = x0): csr  rs1
  CSRR csr, rd (funct3 = CSRRS, rs1 = x0): rd  csr
CSR
funct3
rs1
rd
opcode
12
5
3
5
7
Notes: I currently implement the 4 CSRs (cycle, instret, hartid, mtohost) in the slide.
There are many other CSRs: e.g. mstatus
We need to implement mepc and mcause when handling exceptions.
cycle, instret, hartid – read-only
mtohost – write-only
  Complete instructions to access CSR: CSRRW[I], CSRRS[I], CSRRC[I]
These instructions will read-modify-write CSRs.
CSRR and CSRW are easiest cases where only read or write happens.

## Slide 52: Summary of RISC-V Instruction Format

## Slide 53: Assembly Code VS Binary
Its too tedious to write programs in binary
To simplify writing programs, assemblers provide:
  mnemonics for instructions
    add x1, x2, x3
  pseudo instructions
    mov x1, x2 // short for add x1, x2, x0
    li x1, 6175 // short for lui x1, 2 ; addi x1, x1, -2017 (exact sequence depends
    on immediate value)
  symbols for program locations and data
    bnz x1, loop_begin
    lw x1, flag
Assemblers translate programs into machine code for the processor to execute
Notes: Immediate encoding is also messy and require automation

## Slide 54: GCD in C
// require: a >= 0 && b > 0
int gcd(int a, int b) {
int t;
while(a != 0) {
if(a >= b) {
a = a - b;
}
else {
t = a;
a = b;
b = t;
}
}
return b;
}
Example:
Assume a=12 b=4
a>=b
a=a-b = 12-4 = 8
a>=b
a=a-b=8-4=4
a>=b
a=a-b=4-4= 0
a==0
return b

## Slide 55: GCD in RV Assembly Language
// a: x1, b: x2, t: x3
begin:
beq x1, x0, done // if(x1 == 0) goto done
blt x1, x2, b_bigger // if(x1 < x2) goto b_bigger
sub x1, x1, x2 // x1 := x1 - x2
j begin // was a jump inst to skip over else part
b_bigger:
add x3, x1,x0 // x3 := x1
add x1, x2,x0 // x1 := x2
add x2, x3,x0 // x2 := x3
j begin // goto begin
done: // now x2 contains the gcd
Another way to swap X1 and X2
without using X3 is:
X1 = X1 xor X2
X2 = X1 xor X2
X1 = X1 xor X2
If a and b are passed in as
*a,*b, two pointers. The compiler
would not allocate *a, and *b
to registers, because a,b may
point to the same memory
location
Pseudo instruction
Notes: Was interesting during the time when the number of registers were only 8
Be careful: if a, and b are passed in as two pointers: *a *b, then the compiler could not allocate them in registers because they may point to the same memory location.

## Slide 56: Application Binary Interface (ABI)
Calling convention in ABI defines specifies rules for register usage in passing arguments and results for function calls
  Callee-saved registers vs Caller-saved registers
Assigns aliases for registers x1-x31
  a0 to a7 – function argument registers (caller-saved)
  a0 and a1 – function return value registers
  s0 to s11 – Saved registers (callee-saved)
  t0 to t6 – temporary registers (caller-saved)
  ra – return address (caller-saved)
  sp – stack pointer (callee-saved)
  gp (global pointer), and tp (thread pointer) point to specific locations in memory used by the program for global and thread-local variables respectively
Notes: Why do we need calling convention? For interoperability cross different compilers, different software, different library.
If not well defined, arguments may not be passed by registers!!!

## Slide 57: Mapping between Physical Reg to ABI Reg
Names | RISC-V registers | ABI register name
Zero register | X0 | 
Return Address | X1 | ra
Stack pointer | X2 | sp
Global pointer | X3 | gp
Thread pointer | X4 | tp
Temporary | X5-X7, X28-X31 | t0-t6
Saved registers | X8-X9, X18-X27 | s0-s11
Function arguments | X10-X17 | a0-a7

## Slide 58: Mapping between Physical Reg to ABI Reg
Names | RISC-V registers | ABI register name
Zero register | X0 | 
Return Address | X1 | ra
Stack pointer | X2 | sp
Global pointer | X3 | gp
Thread pointer | X4 | tp
Temporary | X5-X7, X28-X31 | t0-t6
Saved registers | X8-X9, X18-X27 | s0-s11
Function arguments | X10-X17 | a0-a7
Caller save
Callee save

## Slide 59: Calling GCD (Using the ABI)
// assume we want to do the gcd of s0 and s1
// and put the result in s2
mv a0, s0
mv a1, s1
addi sp, sp, -8 // allocate stack space for saving registers
in the stack as needed by the caller
sw t0, 4(sp)
sw t1, 0(sp)
jal gcd // call the gcd function
lw t0, 4(sp) // restoring caller-saved registers
lw t1, 0(sp)
addi sp, sp, 8 // pop off the stack space
mv s2, a0
preparing arguments in a0, a1, etc.
Temporary save
Temporary restore

## Slide 60: GCD in RISC-V Assembler Using the ABI
// a: a0, b: a1, t: t0
gcd:
beqz a0, done
blt a0, a1, b_bigger
sub a0, a0, a1
j gcd
b_bigger:
mv t0, a0
mv a0, a1
mv a1, t0
j gcd
done: // now a1 contains the gcd
mv a0, a1 // move to a0 for returning
ret // jr ra
argument
temporary
ABI dictates that the result must come back in a0
// a: x10, b: x11, t: x5
begin:
beqz x10, done
blt x10, x11, b_bigger
sub x10, x10, x11
j begin
b_bigger:
mv x5, x10
mv x10, x11
mv x11, x5
j begin
done:

## Slide 61: Multiply
mul x1, x2, x3 is an instruction in the ‘M’ extension (x1 := x2 * x3)
  If ‘M’ is NOT implemented, this is an illegal instruction
What happens if we run code from an RV32IM machine on an RV32I machine?
  mul causes an illegal instruction exception
An exception handler can take over and abort the program or emulate the instruction

## Slide 62: Exception handling
When an exception is caused
  Hardware saves the information about the exception in CSRs:
    mepc – exception PC
    mcause – cause of the exception
    mstatus.mpp – privilege mode of exception
  Processor jumps to the address of the trap handler (stored in the mtvec CSR) and increases the privilege level
An exception handler, a software program, takes over and performs the necessary action

## Slide 63: Software for interrupt handling
Hardware transfers control to the common software interrupt handler (CH) which:
  Saves all GPRs into the memory pointed by mscratch
  Passes mcause, mepc, stack pointer to the IH (a C function) to handle the specific interrupt
  On the return from the IH, first determine which instruction to return to, and modify mepc (+4 or +2)
  Loads all GPRs from the memory
  Execute ERET, which does:
    set pc to mepc
    pop mstatus (mode, enable) stack
IH
IH
IH
CH
1
2
3
4
5
GPR

## Slide 64: Common Interrupt Handler- SW (1)
common_handler: # entry point for exception handler # get the pointer to HW-thread local stack
csrrw sp, mscratch, sp # swap sp and mscratch
# save x1, x3 ~ x31 to stack (x2 is sp, save later)
addi sp, sp, -128
sw x1, 4(sp)
sw x3, 12(sp)
...
sw x31, 124(sp)
# save original sp (now in mscratch) to stack
csrr s0, mscratch # store mscratch to s0
sw s0, 8(sp)

## Slide 65: Illegal Instruction IH (in C)
long illegal_inst_ih(long cause, long epc, long *regs)
{ uint32_t inst = *((uint32_t*)epc); // fetch inst
// check opcode & function codes
if((inst & MASK_MUL) == MATCH_MUL) {
// is MUL, extract rd, rs1, rs2 fields
int rd = (inst >> 7) & 0x01F;
int rs1 = ...; int rs2 = ...;
// emulate regs[rd] = regs[rs1] * regs[rs2]
emulate_multiply(rd, rs1, rs2, regs);
return epc + 4; // done, resume at epc+4
} else abort();
}

## Slide 66: Instruction Set Design Issues
Some questions for you to keep in mind. We will revisit them
after Chapter 4 (Data Path implementation)
  Should we have 1024 general-purpose registers in the ISA?
  Should we use Compare and Branch or Condition-Code-based branches?
  Should we support fast procedure calls with a single instruction?
  Should we support 3-operand or 4-operand instruction formats?
  Should we adopt register pairs to handle wider data requirements?
  Should we support post-increment memory loads?
  Should we support a dedicated bit for static branch prediction?
  …..