## Slide 1: CSC3050 – Computer Architecture
Quiz 4 (group competition)

## Slide 2
Example 1
Which of the following storages are considered as caches?
A BTB
A TLB
A L3 cache
A branch prediction table
Answer: 1,2,3,4

## Slide 3
Are you ready ?

## Slide 4
In computer architecture, the term “memory wall” refers to which of the following?
The gap between the disk and the memory
The gap between DRAM and SRAM
The gap between the registers and the L1 data cache
The gap between CPU and the main memory (DRAM)
Answer: 4

## Slide 5
2) Which of the following information are stored in the cache?
Data of the cache block
Set number
The valid bit
The address tag
The dirty bit
Answer: 1,3,4,5

## Slide 6
3) From the earliest days, programmers have always wanted large, fast and cheap memory. How do we give programmers what they want?
via Memory Hierarchy
via Predictions
via Virtual Memory
via Virtual Machines
via Vector architectures
Answer: 1,3

## Slide 7
4) In a memory hierarchy, which layers are managed by the compiler or the programmers?
The registers
The L1/L2/L3 caches
The local memory
The physical memoy
Answer: 1,3

## Slide 8
5) Assume the cache size is 64KB, and the line size 64B
Which of the following are correct?
In a direct mapped cache, there are 1024 sets
In a two-way set associative cache, there are two sets
In a fully associative cache, there is only one set
In a eight-way set associative cache, there are 8 sets
Answer: 1,3

## Slide 9
6) Which of the following caches may not have the tag bits when used in practice ?
An instruction cache
A level 3 (L3) cache
A branch prediction table
A TLB
Answer: 3

## Slide 10
7) Assume the same cache size and the same line size, which of the following statements are always true?
A direct mapped cache is faster than set associative caches
A fully associative cache has the lowest cache miss rate
A direct mapped cache has the lowest tag overhead
Replacement in a direct mapped cache is the simplest
Answer: 3,4

## Slide 11
8) The instruction cache is usually easier to manage than the data cache, why?
It does not need the dirty bit
It does not need the valid bit
It does not need to handle writes from the processor
It does not need the tag bits
Answer: 1, 3
Notes: RISC-V has no opcode as 0000000 (illegal instruction)

## Slide 12
9) If minimizing the tag space is the primary goal, which of the following cache features should be used ?
Set associative caches
Direct mapped caches
Write no-allocate policy
Large cache blocks (lines)
Inclusive caches
Answer: 2, 4

## Slide 13
10) Modern processors often have L1/L2/L3 caches implemented in a processor. Which of the following statements are true?
1) The primary goal of L3 cache is to reduce the memory traffic to the memory
2) The primary goal of L1 cache is to have fast hit time
3) The L3 cache should adopt write-through policy
4) The L2 is always multiple times larger than L1
Answer: 1,2

## Slide 14
11) What are the four type of cache misses ?
  Compulsory misses, Conflict misses, Capacity misses, Coherence misses
  Cold misses, Collision misses, Capacity misses, Coherence misses
  Combined misses, Conformant misses, Contiguous misses, Conditional misses
  Cool misses, Conflict misses, Inclusive misses, Exclusive misses
Answer: 1,2

## Slide 15
12) What are the advantages of using a large cache line size ?
It exploits more spatial locality
It exploits more temporal locality
It saves tag space
It could reduce compulsory misses
Answer: 1,3,4

## Slide 16
13) L1 caches are usually split into L1I and L1D. What are the advantages of this splitting.
For a higher hit rate
For a greater access bandwidth
I-cache can be managed differently from D-cache
For a higher associativity
Answer: 2,3

## Slide 17
14) Cray vector supercomputers did not have data caches, but they use vector loads and stores. Compared to modern computers with data caches, what is the weakness of Cray Vector Supercomputers?
They do not take advantages of memory spatial locality
They do not take advantages of memory temporal locality
Their instruction fetching would be much slower
They are incapable of taking advantages of localities for languages with extensive pointer aliasing.
Answer: 4

## Slide 18
15) My computer has a two-way set associative cache with 4KB and 32B line size, which of the following memory reference sequences would run into conflict misses ?
1) 0x01ABC000, 0x01ABC004, 0x01ABC010, 0x01ABC002,
2) 0x01ABC000, 0x01ABB004, 0x01ABD000, 0x01ABA010,
3) 0x01ABC000, 0x01ABC020, 0x01ABC030, 0x01ABC040,
4) 0x01ABC020, 0x01ABC030, 0x01ABC02A, 0x01ABC03A,
Answer: 2

## Slide 19
16) My cache supports both write allocate and write no-allocate policy, it is controlled by a bit in the store instruction. Under what condition, the store instruction should turn on “write-no-allocate”?
In the memcpy(a,b,n) lib call when n is large
When storing local variables in a procedure
When storing a struct member (e.g. st.a or st->a)
In the memset(a,b,n) lib call when n is large.
Answer: 1,4

## Slide 20
17) Which of the following cache features would require greater bus and memory bandwidth?
Large cache lines
Cache prefetching
Non-blocking caches
Exclusive, multi-level, write-back caches
Write-through caches
Answer: 1,2,3,5

## Slide 21
18) For a single cycle data path design, if the D-cache miss rate is 5%, 40% of instructions are load/stores, and the memory latency is 100 cycles. What would be the average CPI?
2.0
1.4
1.6
3.0
Answer: 4

## Slide 22
19) For many years, AMAT (Average Memory Access Time) was used to estimate the impact of caches to the performance of a program. However, AMAT has become less accurate recently because of
1) Caches are getting larger, misses are now rare, so they could be ignored
2) Caches are now non-blocking, multiple misses may be handled in parallel. The overlapped miss handling is not part of the AMAT equation.
3) AMAT was designed for single level cache, now most caches are multi-level caches
4) Out-of-order execution allows instructions continue to execute, so that the cache miss penalty could be partially hidden
Answer: 2,4

## Slide 23
20) Which of the following statements about the “snoopy” cache are true?
It is design to maintain cache coherence for bus connected multi-processor systems
It is designed as a watch dog for preventing illegal cache references
It is designed for dara security enforcement
It is designed to peeking data in neighbor’s caches
Answer: 1

## Slide 24
21) Which of the following could reduce conflict misses incurred in a direct mapped L1 cache?
Increase the cache sizes
Increase the cache block (line) sizes
Add a victim cache
Change to set associative cache
Use the best replacement algorithm
Answer: 1,3,4

## Slide 25
22) Which of the following are often useful in reducing cache capacity misses?
Increase the cache sizes
Increase the cache block (line) sizes
Add one victim cache
Change to set associative cache
Cache prefetching
Answer: 1,5

## Slide 26
23) MSHR (Miss Status Handling Registers) are used to track multiple outstanding cache misses. Each level of cache has its own MSHR. On a multicore chip, the number of entries in the L3 MSHR would likely be influenced by
The memory latency
The memory bus width
The size of the L2 cache
The number of cores sharing the L3
Answer: 1,2,4

## Slide 27
24) I-cache does not take stores from the processor. However, modern applications use “instruction patching” or “JIT” code generation to either modify instructions or generate a new section of code for subsequent execution. Which of the following solutions could work.
Flush the I-cache to purge all old instructions
Invalidate the I-cache lines containing the instructions
Flush the data caches
Maintain coherence between I- and D-cache: any updates to the D-cache will also write into the respective lines in I-cache.
Answer: 1,2,4